## Slide 1: SD-WAN based light-weight cloud assisted multicast
Balaji Venkat Venkataswami
Ganesh Chennimalai Sankaran
© 2019

## Slide 2: Problem Statement
Multicast facilitation is a requirement among set of sites sought to be connected through SD-WAN
With NO explicit multicast PIM state in the WAN, multicasting ought to be facilitated.
Must keep the multicast state restricted to the SD-WAN sites.
With minimal control plane exchanges multicasting ought to be facilitated.
Data plane ought to be simple with context indication in a key that facilitates replication.
Setup of the multicast source and receivers should be minimal and seamless.
No Multicast PIM state in the cloud at all should be required !!!
  Forwarding state in Cloud Replicators are not PIM based.
  Just Source Edge box from which to receive the stream
  And Destination Edge boxes to which stream is to be replicated.
Multicast state within a site should be spliced with the minimal state in the cloud facilitator.

## Slide 3: Methodology of the invention
Components of the scheme
  Cloud replicator
  Edge SD-WAN box at branch offices and HQ sites
  Web based multicast orchestrator
  SDN Controller than can be in-built with the Orchestrator or exist separately.
  Tunnels between Edge box and cloud replicator
    Includes source tunnel from source branch site/HQ site
    Includes destination tunnels to branch sites/HQ site
    Preferable GRE based
      Where the GRE key provides the context.
  Multicast state within the site to facilitate multicast replication within the site.
  For PIM-SM all Edge Boxes stated to be Rendezvous Points (RPs) for their respective sites.
  At the source site the Edge box is the RP as well building the Shortest Path Tree to source on the same interface on which it replicates for other receivers (akin to router on a stick).
  Alternatively at the source site any router (1 or more hops away from source host) could be considered the RP. The Edge box at the source site could be configured from the Controller with the RP address through the Web based Orchestrator interface.
  Load balancers in the cloud that help in sharing the cloud replicators’ load.
  No PIM state in the cloud / SDN Controller / Orchestrator.

## Slide 4: Control Plane sequence
Orchestrator along with Controller allocates
  (a) GRE key context for multicast stream and CR-IP address
  (b) Multicast class D address for stream
  (c) Designates source of multicast stream
  (d) Establishes state at Edge box of source for GRE tunnel encapsulation splicing mcast (S,G) with GRE tunnel with key context and CR-IP from (a).
  (e) Establishes state at Edge boxes of receivers for GRE tunnel decapsulation splicing mcast (S,G) with GRE tunnel with key context and CR-IP from (a).
  (e.1) Splices incoming GRE key context from Edge box at Source site with outgoing Edge-Box-IP addresses as destinations for replicated stream.
  (e.2) Creates replication state in the CRs allocated which contains list of Destination Edge boxes for the Source Edge Box representing the source to which replications needs to be done.
  (f) following (d) facilitates PIM (S,G) state instantiation from Edge box at source site to the actual multicast source host/server including all intervening routers and switches.
  (g) following (e) facilitates PIM(S,G) state instantiation from actual receivers through IGMP join and at all intermediate routers and switches within the receiver site through PIM join all the way to the Edge box on the receiver site.
  All of this takes place with the requisite condition that local replication occurs at the source site through regular multicast IGMP and PIM joins.

## Slide 5: Data plane sequence
(1) Source at Source site sends packet based on PIM multicast state to local receivers and Edge box at source site.
(2) At Edge box lookup is done using control plane state (d) that GRE encapsulates the packet with key context from control plane state (a).
(3) Packet travels to a load-balancer where the flow is sent to one of many cloud replicators.
(4) Cloud replicator replicates the stream as is with changes to the destination IP address.
  The destination IP address in the outer header is set to that of the Edge boxes of receiver sites assigned for replication at the CR (Cloud replicator).
  The source address is set to that of the cloud replicator in the outer header of the GRE encapsulation.
  Packet is sent on its way after compression if required. Compression state is indicated in the GRE key context.
(5) Packet reaches the Edge box at the receiver sites where…
  At Edge box lookup is done using control plane state (e) that GRE decapsulates the packet with the key context from control plane State (a).
  Packet travels through intermediate routers and switches to the actual receiver end hosts using the lookup at the multicast PIM state thereof.

## Slide 6: Compression and Decompression
Compression can be done at the source of the multicast stream within the source site.
Or Compression could be facilitated at the Cloud Replicator where the CR could be one of many.
  Efficiency in this case is increased since the stream needs to be compressed just once at the assigned CR.
Decompression is done at the destination end host which is the receiver.
A part of the GRE key context space is used to designate compression state whether compressed or decompressed.
  Also additional state information on compression algorithm to be used can be instantiated at the receiver end host and at the source host in the source site through the Web orchestrator.
  At the receiver end host the user could use a hyper link that receives the compression/decompression algorithm state information and thus uses it to decompress the said stream if at all the GRE key context indicates it is compressed. There could be other ways of instantiating this state as well.

## Slide 7: CR and orchestration
The Web based orchestrator can be accessed by the customer using a self-service portal that
  Allocates a set of CRs for the customer based on the number of replications to be done.
  Allocates a Load-balancer for the said stream for the customer
  Allocates Multicast D address from a pool for the customer.
  Allocates GRE key context from a pool for the customer’s stream.
  Creates hyperlinks in an email or any other communication mechanism that will convey the context to the receiver end hosts.
    A registry of available streams for viewing can also be created and used to facilitate the receivers to link into the stream.
    Mechanisms such as a HTTP link could be the facilitating trigger to join into the stream from any of the sites in the customers’ set of branch offices including the HQ/Hub site.
  Replicator is totally agnostic of PIM and any other protocols
  CR is a lightweight replicator of one to many as configured through the WO + Controller.
  No PIM replication state is maintained in the Cloud Replicator (CR).

## Slide 8: Load balancers and the CRs
The load balancer
  Receives the stream from the source
  Possibly could replicate the packet to a set of CRs
  Which in turn the CRs would replicate the packets to the set of destination Edge boxes of the customer that are assigned to that CR.
  The decision of which destination site to replicate to by the CR could be arrived at by allocating N destinations where N = Number-of-sites/Number of CRs to each CR in the set allocated by the WO (Web Orchestrator).

## Slide 9: Chained Replication at more than one location in the cloud
It is possible that the CRs allocated in a cloud location may be overloaded with respect to replication for all sites involved if the number of sites exceeds a threshold.
In such a case…
  Chained replication could be deployed where
  The initial set of CRs at a central location (cloud center) replicate and send some of the streams off to a (cloud local) e.g, a data center (public cloud) nearer to a set of destination sites from where...
    The stream is further replicated to a further set of destination sites

## Slide 10: Advantages and Novelty
This provides a mechanism to facilitate multicast that is
  Easy to deploy.
  Provides a lightweight mechanism for the SDN controller and Orchestrator
    Controller and Orchestrator could exist as a lightweight VM that dispenses the replication.
    Could be a plugin for existing SDN controllers.
  Easy to provision at the source and destination end hosts.
  Easy to replicate at scale in the cloud
  Requires software based solutions with the CRs being spun off as a VM/Container
  Uses light-weight tunneling at the Edge boxes where such tunnels exist between the Edge boxes and the CR + Load-balancer.
  Uses the splicing of PIM state with the tunnels as the data plane stream delivery mechanism.
  Number of CRs can easily be scaled by merely spawning a larger number of VMs for replication (CRs).
  Monitoring could be done on the Edge boxes and the CRs to facilitate statistics collection and reporting on bandwidth used, delay experienced which in turn can tune the compression algorithms.
  A purely web based deployment mechanism will be in vogue.
  There is no PIM state in the Internet of any kind
  No configuration of PIM in the WAN and no PIM-based forwarding state in the Cloud Replicators.
    Seamlessly CR replicates whatever is given to it.
    CR is a thin replicator with minimal state.
    Is totally agnostic of PIM and other multicast protocols.
  Will be applicable to IPv6 as well with multicast v6 state restricted to within the sites in the SD-WAN deployment.
  The IP-in-IP encapsulation can be GRE or something propreitary to this SD-WAN multicast solution.

## Slide 11: Prior art and references…
TODO : References and prior art.
Comparison with
- Viptela (Cisco)
- Aryaka
- Velocloud
- Versa
- Netscaler SD-WAN
- 128 Technologies
- Nuage Networks
- Juniper
- and a few others.